## Slide 1: Microprocessor System Design AVR Microcontroller
Omid Fatemi

## Slide 2: Contents
Introduction

## Slide 3: Introduction
CPU for Computers
No RAM, ROM, I/O on CPU chip itself
Example Intel’s x86, Motorola’s 680x0
CPU
General-Purpose Micro-processor
RAM
ROM
I/O Port
Timer
Serial COM Port
Data Bus
Address Bus
General-Purpose Microprocessor System
Many chips on mother’s board
General-purpose microprocessor
Notes: Intel’s x86 8086,8088,80386,80486, Pentium
Motorola’s 680x0 68000, 68010, 68020,68030,6040

## Slide 4: Microcontroller
RAM
ROM
I/O Port
Timer
Serial COM Port
Microcontroller
CPU
A smaller computer
On-chip RAM, ROM, I/O ports...
Example AVR, Intel’s 8051, Zilog’s Z8 and PIC 16X
A single chip

## Slide 5: Microprocessor vs. Microcontroller
Microprocessor
CPU is stand-alone, RAM, ROM, I/O, timer are separate
designer can decide on the amount of ROM, RAM and I/O ports.
More consumption power
More computing power
versatility
general-purpose
Microcontroller
CPU, RAM, ROM, I/O and timer are all on a single chip
fix amount of on-chip ROM, RAM, I/O ports
for applications in which cost, power and space are critical
Less applications
Notes: Versatility: any number of applications for PC

## Slide 6: Embedded System
Embedded system means the processor is embedded into that application.
An embedded product uses a microprocessor or microcontroller to do one task only.
In an embedded system, there is only one application software that is typically burned into ROM.
Example printer, keyboard, video game player
Notes: A printer is an example of embedded system since the processor inside it performs one task only.

## Slide 7: Three Criteria in Choosing a Microcontroller
meeting the computing needs of the task efficiently and cost effectively
  speed, the amount of ROM and RAM, the number of I/O ports and timers, size, packaging, power consumption
  easy to upgrade
  cost per unit
availability of software development tools
  assemblers, debuggers, C compilers, in circuit emulator, simulator, technical support
wide availability and reliable sources for the microcontroller.

## Slide 8: General Purpose Microprocessors vs. Microcontrollers
General
Purpose
Micro
processor
RAM
ROM
Timer
Serial
COM
Port
IO
Port
Data BUS
Address BUS
Control BUS
CPU
RAM
ROM
I/O
Timer
Serial
Port
General Purpose Microprocessors
Microcontrollers

## Slide 9: Most common microcontrollers
8-bit microcontrollers
  AVR
  PIC
  HCS12
  8051
32-bit microcontrollers
  ARM
  PIC32

## Slide 10: AVR internal architecture

## Slide 11: AVR different groups
Classic AVR
  e.g. AT90S2313, AT90S4433
Mega
  e.g. ATmega8, ATmega32, ATmega128
Tiny
  e.g. ATtiny13, ATtiny25
Special Purpose AVR
  e.g. AT90PWM216,AT90USB1287
Notes: Plastic Dual Inline Package
Thin Quad Flat Package
Micro Lead Frame
Small Outline integrated circuit
Low profile Quad flat

## Slide 12: Let’s get familiar with the AVR part numbers
ATmega128
ATtiny44
Atmel
group
Flash =128K
Atmel
Flash =4K
AT90S4433
Atmel
Classic group
Flash =4K
Tiny group

## Slide 13: Introduction to Assembly Chapter 2
The AVR microcontroller
and embedded
systems
using assembly and c

## Slide 14: Topics
AVR’s CPU
  Its architecture
  Some simple programs
Data Memory access
Program memory
RISC architecture

## Slide 15: AVR’s CPU
AVR’s CPU
  ALU
  32 General Purpose registers (R0 to R31)
  PC register
  Instruction decoder
CPU
PC
ALU
registers
R1
R0
R15
R2
…
R16
R17
…
R30
R31
Instruction Register
Instruction decoder
SREG:
I
T
H
S
V
N
C
Z

## Slide 16: Some simple instructions 1. Loading values into the general purpose registers
LDI (Load Immediate)
LDI Rd, k
  Its equivalent in high level languages:
  Rd = k
Example:
  LDI R16,53
    R16 = 53
  LDI R19,132
  LDI R23,0x27
    R23 = 0x27
CPU
PC
ALU
registers
R1
R0
R15
R2
…
R16
R17
…
R30
R31
Instruction Register
Instruction decoder
SREG:
I
T
H
S
V
N
C
Z

## Slide 17: Some simple instructions 2. Arithmetic calculation
There are some instructions for doing Arithmetic and logic operations; such as:
  ADD, SUB, MUL, AND, etc.
ADD Rd,Rs
  Rd = Rd + Rs
  Example:
  ADD R25, R9
    R25 = R25 + R9
  ADD R17,R30
    R17 = R17 + R30
CPU
PC
ALU
registers
R1
R0
R15
R2
…
R16
R17
…
R30
R31
Instruction Register
Instruction decoder
SREG:
I
T
H
S
V
N
C
Z

## Slide 18: A simple program
Write a program that calculates 19 + 95
LDI R16, 19 ;R16 = 19
LDI R20, 95 ;R20 = 95
ADD R16, R20 ;R16 = R16 + R20
CPU
PC
ALU
registers
R1
R0
R15
R2
…
R16
R17
…
R30
R31
Instruction Register
Instruction decoder
SREG:
I
T
H
S
V
N
C
Z

## Slide 19: A simple program
Write a program that calculates 19 + 95 + 5
LDI R16, 19 ;R16 = 19
LDI R20, 95 ;R20 = 95
LDI R21, 5 ;R21 = 5
ADD R16, R20 ;R16 = R16 + R20
ADD R16, R21 ;R16 = R16 + R21
LDI R16, 19 ;R16 = 19
LDI R20, 95 ;R20 = 95
ADD R16, R20 ;R16 = R16 + R20
LDI R20, 5 ;R20 = 5
ADD R16, R20 ;R16 = R16 + R20

## Slide 20: Some simple instructions 2. Arithmetic calculation
SUB Rd,Rs
  Rd = Rd - Rs
Example:
  SUB R25, R9
    R25 = R25 - R9
  SUB R17,R30
    R17 = R17 - R30
CPU
PC
ALU
registers
R1
R0
R15
R2
…
R16
R17
…
R30
R31
Instruction Register
Instruction decoder
SREG:
I
T
H
S
V
N
C
Z

## Slide 21: Some simple instructions 2. Arithmetic calculation
INC Rd
  Rd = Rd + 1
Example:
  INC R25
    R25 = R25 + 1
DEC Rd
  Rd = Rd - 1
Example:
  DEC R23
    R23 = R23 - 1
CPU
PC
ALU
registers
R1
R0
R15
R2
…
R16
R17
…
R30
R31
Instruction Register
Instruction decoder
SREG:
I
T
H
S
V
N
C
Z

## Slide 22: Data Address Space
LDS Rd, addr ;Rd = [addr]
Example:
LDS R1, 0x60
LDS (Load direct from data space)
STS addr,Rd ;[addr]=Rd
Example:
STS 0x60,R15 ; [0x60] = R15
STS (Store direct to data space)
Example: Write a program that stores 55 into location 0x80 of RAM.
Solution:
LDI R20, 55 ;R20 = 55
STS 0x80, R20 ;[0x80] = R20 = 55
Example: Write a program that copies the contents of location 0x80 of RAM into location 0x81.
Solution:
LDS R20, 0x80 ;R20 = [0x80]
STS 0x81, R20 ;[0x81] = R20 = [0x80]
Example: Add contents of location 0x90 to contents of location 0x95 and store the result in location 0x313.
Solution:
LDS R20, 0x90 ;R20 = [0x90]
LDS R21, 0x95 ;R21 = [0x95]
ADD R20, R21 ;R20 = R20 + R21
STS 0x313, R20 ;[0x313] = R20
Example: What does the following instruction do?
LDS R20,2
Answer:
It copies the contents of R2 into R20; as 2 is the address of R2.
Example: Store 0x53 into the SPH register. The address of SPH is 0x5E
Solution:
LDI R20, 0x53 ;R20 = 0x53
STS 0x5E, R20 ;SPH = R20

## Slide 23: Data Address Space
IN Rd,IOaddress ;Rd = [addr]
Example:
IN R1, 0x3F ;R1 = SREG
IN R17,0x3E ;R17 = SPH
IN (IN from IO location)
OUT IOAddr,Rd ;[addr]=Rd
Example:
OUT 0x3F,R12 ;SREG = R12
OUT 0x3E,R15 ;SPH = R15
OUT (OUT to IO location)
Example:
OUT SPH,R12 ;OUT 0x3E,R12
IN R15,SREG ;IN R15,0x3F
Using Names of IO registers
Example: Write a program that adds the contents of the PINC IO register to the contents of PIND and stores the result in location 0x90 of the SRAM
Solution:
IN R20,PINC ;R20 = PINC
IN R21,PIND ;R21 = PIND
ADD R20,R21 ;R20 = R20 + R21
STS 0x90,R20 ;[0x90] = R20

## Slide 24: Status Register (SREG)
CPU
PC
ALU
registers
R1
R0
R15
R2
…
R16
R17
…
R30
R31
Instruction Register
Instruction decoder
SREG:
I
T
H
S
V
N
C
Z
SREG:
Carry
Zero
Negative
oVerflow
Sign
N+V
Half carry
Temporary
Interrupt
H
S
V
N
C
Z
T
I
Example: Show the status of the C, H, and Z flags after the addition of 0x38 and 0x2F in the following instructions:
LDI R16, 0x38 ;R16 = 0x38
LDI R17, 0x2F ;R17 = 0x2F
ADD R16, R17 ;add R17 to R16
Solution: 1
$38 0011 1000
+ $2F 0010 1111
$67 0110 0111 R16 = 0x67
C = 0 because there is no carry beyond the D7 bit.
H = 1 because there is a carry from the D3 to the D4 bit.
Z = 0 because the R16 (the result) has a value other than 0 after the addition.
Example: Show the status of the C, H, and Z flags after the addition of 0x9C and 0x64 in the following instructions:
LDI R20, 0x9C
LDI R21, 0x64
ADD R20, R21 ;add R21 to R20
Solution: 1
$9C 1001 1100
+ $64 0110 0100
$100 1 0000 0000 R20 = 00
C = 1 because there is a carry beyond the D7 bit.
H = 1 because there is a carry from the D3 to the D4 bit.
Z = 1 because the R20 (the result) has a value 0 in it after the addition.
Example: Show the status of the C, H, and Z flags after the subtraction of 0x23 from 0xA5 in the following instructions:
LDI R20, 0xA5
LDI R21, 0x23
SUB R20, R21 ;subtract R21 from R20
Solution:
$A5 1010 0101
- $23 0010 0011
$82 1000 0010 R20 = $82
C = 0 because R21 is not bigger than R20 and there is no borrow from D8 bit.
Z = 0 because the R20 has a value other than 0 after the subtraction.
H = 0 because there is no borrow from D4 to D3.
Example: Show the status of the C, H, and Z flags after the subtraction of 0x73 from 0x52 in the following instructions:
LDI R20, 0x52
LDI R21, 0x73
SUB R20, R21 ;subtract R21 from R20
Solution:
$52 0101 0010
- $73 0111 0011
$DF 1101 1111 R20 = $DF
C = 1 because R21 is bigger than R20 and there is a borrow from D8 bit.
Z = 0 because the R20 has a value other than zero after the subtraction.
H = 1 because there is a borrow from D4 to D3.
Example: Show the status of the C, H, and Z flags after the subtraction of 0x9C from 0x9C in the following instructions:
LDI R20, 0x9C
LDI R21, 0x9C
SUB R20, R21 ;subtract R21 from R20
Solution:
$9C 1001 1100
- $9C 1001 1100
$00 0000 0000 R20 = $00
C = 0 because R21 is not bigger than R20 and there is no borrow from D8 bit.
Z = 1 because the R20 is zero after the subtraction.
H = 0 because there is no borrow from D4 to D3.
Notes: BRBC s, k Branch if Status Flag Cleared if (SREG(s) = 0) then PC ¬ PC+k + 1 None 1 / 2
BREQ k Branch if Equal if (Z = 1) then PC ¬ PC + k + 1 None 1 / 2
BRNE k Branch if Not Equal if (Z = 0) then PC ¬ PC + k + 1 None 1 / 2
BRCS k Branch if Carry Set if (C = 1) then PC ¬ PC + k + 1 None 1 / 2
BRCC k Branch if Carry Cleared if (C = 0) then PC ¬ PC + k + 1 None 1 / 2
BRSH k Branch if Same or Higher if (C = 0) then PC ¬ PC + k + 1 None 1 / 2
BRLO k Branch if Lower if (C = 1) then PC ¬ PC + k + 1 None 1 / 2
BRMI k Branch if Minus if (N = 1) then PC ¬ PC + k + 1 None 1 / 2
BRPL k Branch if Plus if (N = 0) then PC ¬ PC + k + 1 None 1 / 2
BRGE k Branch if Greater or Equal, Signed if (N Å V= 0) then PC ¬ PC+ k + 1 None 1 / 2
BRLT k Branch if Less Than, Signed if (N Å V= 1) then PC ¬ PC + k + 1 None 1 / 2
BRHS k Branch if Half Carry Flag Set if (H = 1) then PC ¬ PC + k + 1 None 1 / 2
BRHC k Branch if Half Carry Flag Cleared if (H = 0) then PC ¬ PC + k + 1 None 1 / 2
BRTS k Branch if T Flag Set if (T = 1) then PC ¬ PC + k + 1 None 1 / 2
BRTC k Branch if T Flag Cleared if (T = 0) then PC ¬ PC + k + 1 None 1 / 2
BRVS k Branch if Overflow Flag is Set if (V = 1) then PC ¬ PC + k + 1 None 1 / 2
BRVC k Branch if Overflow Flag is Cleared if (V = 0) then PC ¬ PC + k + 1 None 1 / 2
BRIE k Branch if Interrupt Enabled if (I = 1) then PC ¬ PC + k + 1 None 1 / 2
BRID k Branch if Interrupt Disabled if (I = 0) then PC ¬ PC + k + 1 None 1 / 2

## Slide 25: Assembler Directives .EQU and .SET
.EQU name = value
  Example:
.EQU COUNT = 0x25
  LDI R21, COUNT ;R21 = 0x25
  LDI R22, COUNT + 3 ;R22 = 0x28
.SET name = value
  Example:
  .SET COUNT = 0x25
  LDI R21, COUNT ;R21 = 0x25
  LDI R22, COUNT + 3 ;R22 = 0x28
  .SET COUNT = 0x19
  LDI R21, COUNT ;R21 = 0x19
Notes: .set could be changed.
But .equ can’t

## Slide 26: Assembler Directives .INCLUDE
.INCLUDE “filename.ext”
.equ SREG = 0x3f
.equ SPL = 0x3d
.equ SPH = 0x3e
....
.equ INT_VECTORS_SIZE = 42 ; size in words
M32def.inc
.INCLUDE “M32DEF.INC”
LDI R20, 10
OUT SPL, R20
Program.asm

## Slide 27: Assembler Directives .ORG
.ORG address
.ORG 0
LDI R16, 0x25
.ORG 0x7
LDI R17, 0x34
LDI R18, 0x31
Program.asm
00 E205
01 0000
02 0000
03 0000
04 0000
05 0000
06 0000
07 E314
08 E321
09 0000
0A 0000
assembler

## Slide 28: Assembler
Assembly
Machine
Language
assembler

## Slide 29: Flash memory and PC register
16-bit
00 E205
01 E314
02 E321
03 0F01
04 0F02
05 E01B
06 0F01
07 9300
08 0300
09 940C
0A 0009
E205
E314
E321
0F01
0F02
E01B
0F01
9300
0300
940C
0009
0
1
2
3
4
5
6
7
8
9
A
B
LDI R16, 0x25
LDI R17, $34
LDI R18, 0x31
ADD R16, R17
ADD R16, R18
LDI R17, 11
ADD R16, R17
STS SUM, R16
HERE:JMP HERE

## Slide 30: Fetch and execute
Old Architectures
16-bit
00 E205
01 E314
02 E321
03 0F01
04 0F02
05 E01B
06 0F01
07 9300
08 0300
09 940C
0A 0009
Fetch
Execute
Instruct 1
Instruct 2
Instruct 3
Instruct 4

## Slide 31: Pipelining
Pipelining
16-bit
00 E205
01 E314
02 E321
03 0F01
04 0F02
05 E01B
06 0F01
07 9300
08 0300
09 940C
0A 0009
Fetch
Execute
Instruct 1
Instruct 2
Instruct 3
Instruct 4

## Slide 32: How to speed up the CPU
Increase the clock frequency
  More frequency  More power consumption & more heat
  Limitations
Change the architecture
  Pipelining
  RISC

## Slide 33: Changing the architecture RISC vs. CISC
CISC (Complex Instruction Set Computer)
  Put as many instruction as you can into the CPU
RISC (Reduced Instruction Set Computer)
  Reduce the number of instructions, and use your facilities in a more proper way.

## Slide 34: RISC architecture
Feature 1
  RISC processors have a fixed instruction size. It makes the task of instruction decoder easier.
    In AVR the instructions are 2 or 4 bytes.
  In CISC processors instructions have different lengths
    E.g. in 8051
      CLR C ; a 1-byte instruction
      ADD A, #20H ; a 2-byte instruction
      LJMP HERE ; a 3-byte instruction

## Slide 35: RISC architecture
Feature 2: reduce the number of instructions
  Pros: Reduces the number of used transistors
  Cons:
    Can make the assembly programming more difficult
    Can lead to using more memory

## Slide 36: RISC architecture
Feature 3: limit the addressing mode
  Advantage
    hardwiring
  Disadvantage
    Can make the assembly programming more difficult

## Slide 37: RISC architecture
Feature 4: Load/Store
  LDS R20, 0x200
  LDS R21, 0x220
  ADD R20, R21
  STS 0x230, R20

## Slide 38: RISC architecture
Feature 5 (Harvard architecture): separate buses for opcodes and operands
  Advantage: opcodes and operands can go in and out of the CPU together.
  Disadvantage: leads to more cost in general purpose computers.
CPU
Address bus
Data
Memory
Data bus
Control bus
Address bus
Code
Memory
Data bus
Control bus
Fetch
Execute
LDS R20, 0x100
ADD R20, R21
LDS R20, 0x100 ; R20 = [0x100]
ADD R20,R21 ; R20 = R20 + R21

## Slide 39: RISC architecture
Feature 6: more than 95% of instructions are executed in 1 machine cycle

## Slide 40: RISC architecture
Feature 7
  RISC processors have at least 32 registers. Decreases the need for stack and memory usages.
    In AVR there are 32 general purpose registers (R0 to R31)