## Slide 1: Microprocessor System Design
Omid Fatemi
Machine Language Programming
(omid@fatemi.net)

## Slide 2: Class Work #1
Assembly Language

## Slide 3: First Part – Closed Book

## Slide 4: Questions
What do BIU and EU stand for and what are their functions?
CPU uses buses to communicate with what?
Which registers are used for fetching the instruction?
What would be the value of BX after executing these instructions? Mov BL, 98H; Mov BH, E2H;
IF CS=3499H, IP=2500H, find
The logical address
The physical address
The lower and upper range of code segment.
What was the assembly code of this memory content? (B0: MOV AL - 04: ADD AL – 35: MOV AL to memory)
  1500 B0
  1501 21
  1502 04
  1503 42
  1504 35
  1505 D0
  1506 33
Notes: What kind of busses CPU has?
What is the relation between Flags and ALU? What could be the use of Z flag?
What steps does CPU perform to run a program?
Name 2 16-bit and 2 8-bit general register.
DS:BX (where DS: 239F and BX:872A) refers to which physical address?
If both 80286 and 80386SX have 16-bit external data bus, what is the difference between them?

## Slide 5: Second Part – Open discussion and notes

## Slide 6: SUB Instruction
SUB instruction
  SUB des, src ;subtracts the source from destination (result is put in destination)
  Examples:
    MOV AL,55H
    MOV CL,23H
    SUB AL,CL ;
    MOV DH,25H
    SUB DH,34H ; immediate operand
    MOV CX,345H
    SUB CX,[679H]
  Same size (destination and source)

## Slide 7: CMP Instruction
The same as SUB instruction
  CMP des, src ;subtracts the source from destination but the result is not stored. Only the flags are updated.
  Examples:
    MOV AL,55H
    MOV CL,23H
    CMP AL,CL ;
    MOV DH,25H
    CMP DH,34H ; immediate operand
    MOV CX,345H
    CMP CX,[679H]
  Same size (destination and source)

## Slide 8: Conditional Jumps
  CMP AL, 45H
  JNE notequal
  MOV AL, 54H
  notequal:
  …

## Slide 9: Problems
There are two five character strings stored in [150H] and [160H]. Find if the strings match. 0 in CL means mismatch and 1 means match.
Which of the following instructions cannot be coded in 8088 assembly language?
Notes: Write the equivalent assembly code of this:
  If (condition)
  {
    Instruction group 1
  }else{
    Instruction group 2
  }
Assume there are five people with ages stored in [200H] – [204H]. Find the oldest (highest age).