## Slide 1: Microprocessor System Design
Omid Fatemi
Machine Language Programming
(omid@fatemi.net)

## Slide 2: Outline
Assembly programming
Instruction set
Simple program

## Slide 3: Assembly Programming
CPU works in binary
All instructions, data are in binary
Binary instructions (0, 1) are Machine Language
  Or even hexadecimal representation
Assembly language
  Mnemonics
  Low level
Assembler
Linker

## Slide 4: Assembler versus Machine Code
ADD AX, BX ;AX gets value AX+BX
SUB AX, BX ;AX gets value AX-BX
AND AX, BX ;AX gets bitwise AND of AX and BX
INC AX ;AX gets its original value plus 1
DEC BX ;BX gets its original value minus 1
MOV AX, BX ;AX gets values in BX
01 D8
29 D8
21 D8
40
4B
8B C3
01 D8
29 D8
21 D8
40
4B
8B C3
01
D8
29
D8
21
D8
40
4B
8B
C3
a19fe
a19ff
a1a00
a1a01
a1a02
a1a03
a1a04
a1a05
a1a06
a1a07
93ee:db1e
93ee:db1f
93ee:db20
93ee:db21
93ee:db22
93ee:db23
93ee:db24
93ee:db25
93ee:db26
93ee:db27
logical
address
physical
memory
physical
address
ASSEMBLER
LINKER
LOADER

## Slide 5: Instruction Set (AVR)
Syntax: Operands: Program Counter:
ADC Rd, Rr 0 ≤ d ≤ 31, 0 ≤ r ≤ 31 PC ← PC + 1
ADD Rd, Rr 0 ≤ d ≤ 31, 0 ≤ r ≤ 31 PC ← PC + 1
AND Rd, Rr 0 ≤ d ≤ 31, 0 ≤ r ≤ 31 PC ← PC + 1
ANDI Rd, K 16 ≤ d ≤ 31, 0 ≤ K ≤ 255 PC ← PC + 1
BREQ k -64 ≤ k ≤ +63 PC ← PC + k + 1 PC ← PC + 1, if condition is false
CBI A, b 0 ≤ A ≤ 31, 0 ≤ b ≤ 7 PC ← PC + 1
CP Rd, Rr 0 ≤ d ≤ 31, 0 ≤ r ≤ 31 PC ← PC + 1
DEC Rd 0 ≤ d ≤ 31 PC ← PC + 1
IN Rd, A 0 ≤ d ≤ 31, 0 ≤ A ≤ 63 PC ← PC + 1
INC Rd 0 ≤ d ≤ 31 PC ← PC + 1
JMP k 0 ≤ k < 4M PC ← k
LDI Rd, K 16 ≤ d ≤ 31, 0 ≤ K ≤ 255 PC ← PC + 1
MOV Rd, Rr 0 ≤ d ≤ 31, 0 ≤ r ≤ 31 PC ← PC + 1
MUL Rd, Rr 0 ≤ d ≤ 31, 0 ≤ r ≤ 31 PC ← PC + 1
OUT A, Rr 0 ≤ r ≤ 31, 0 ≤ A ≤ 63 PC ← PC + 1
RJMP k -2K ≤ k < 2K PC ← PC + k + 1
SBI A, b 0 ≤ A ≤ 31, 0 ≤ b ≤ 7 PC ← PC + 1

## Slide 6: Instruction Set (8088)
Instructions | Description | Notes
ADC | Add with Carry | destination := destination + source + carry_flag
ADD | Add without Carry | (1) r/m += r/imm; (2) r += m/imm;
AND | Logical AND | (1) r/m &= r/imm; (2) r &= m/imm;
JE | Branch if Equal | if (Z = 1) then PC ← PC + k + 1
JL | Branch if Lower | if (C = 1) then PC ← PC + k + 1
JNE | Branch if Not Equal | if (Z = 0) then PC ← PC + k + 1
JGE | Branch if Same or Higher | if (C = 0) then PC ← PC + k + 1
CALL | call Subroutine | push eip;
CLI | Global Interrupt Disable | I ← 0
CMP | Compare | 
DEC | Decrement by 1 | 
DIV | Unsigned divide | DX:AX = DX:AX / r/m; resulting DX = remainder
XOR | Exclusive OR | (1) r/m ^= r/imm; (2) r ^= m/imm;
IN | Input from port | (1) AL = port[imm]; (2) AL = port[DX]; (3) AX = port[DX];
NOT | Negate the operand, logical NOT | r/m ^= -1;
INT | Call to interrupt | 
INC | Increment by 1 | 
IRET | Return from interrupt | 
JMP | Jump | 
MOV | copies data from one location to another | (1) r/m = r; (2) r = r/m;
MUL | Multiply Unsigned | (1) DX:AX = AX * r/m; (2) AX = AL * r/m;
OR | Logical OR | (1) r/m ¦= r/imm; (2) r ¦= m/imm;
OUT | Output to port | (1) port[imm] = AL; (2) port[DX] = AL; (3) port[DX] = AX;
POP | Pop Register from Stack | r/m = *SP++;
PUSH | Push Register on Stack | *--SP = r/m;
RET | Subroutine Return | It will be translated to a RETN or a RETF
RETN | Return from near procedure | 
RETF | Return from far procedure | 
STI | Global Interrupt Enable | I ← 1
ROR | Rotate right | 
ROL | Rotate left | 
SUB | Subtract without Carry | 

## Slide 7: MOV Instructions
MOV instruction
  MOV des, src ; copy source to destination
  Examples:
    MOV CL,55H
    MOV DL, CL
    MOV AH, DL
    MOV CX,EF28H
    MOV AX, CX
    MOV DI, AX
    MOV BP,DI
  No MOV for flag register
  No immediate load to segment register (only registers)
  Same size (destination and source)

## Slide 8: ADD Instruction
ADD instruction
  ADD des, src ; add the source to destination
  Examples:
    MOV AL,55H
    MOV CL,23H
    ADD AL,CL ;
    MOV DH,25H
    ADD DH,34H ; immediate operand
    MOV CX,345H
    ADD CX,679H
  Same size (destination and source)

## Slide 9: Debug program
R <register name>
A <starting address>
U <start> <end> or U <start> <L number>
G < = starting address> <stop address(es)>
T < = starting address> <number>
F <s> <e> <data> or F <s> <L n> <data>
D <s> <e> or D <s> <L n>
E <address> <data list>

## Slide 10: Segmented Memory
CS
ES
SS
DS
Data
Segment
Stack
Segment
Extra
Segment
Code
Segment
Segment
Registers
Logical, Segmented Address:
0FE6:012Bh
Offset, Index Address:
012Bh
Physical Address:
0FE60h  65120
+ 012Bh  299
0FF8Bh  65149
System
Memory
00000h
FFFFFh

## Slide 11: Program Segments
Code
Data
Stack
80x86 segment registers
  DS, CS, SS, ES
Logical address, physical address
  Physical: 20bit
  Offset: 16 bit
  Logical: segment+offset
How to convert?
Examples of code and data segments

## Slide 12: The Stack
The stack is a memory area intended for storing temporary values.
The stack is accessed by the SS:SP segment/offset combination (StackSegment: StackPointer)
Some instructions make use of the stack area during execution (push, pop, call, ret, many others)
If you need to store temporary values in memory, the stack is the best place to do so.

## Slide 13: Data Storage via the Stack
The word ‘stack’ is used because storage/retrieval of words in the stack memory area is the same as accessing items from a stack of items.
Visualize a stack of boxes. To build a stack, you place box A, then box B, then box C.
A
A
B
A
B
C
Notice that you only have access to the last item placed on the stack (the Top of Stack – TOS). You retrieve the boxes from the stack in reverse order (C then B then A).

## Slide 14: Storing data on X86 stack via PUSH
The SP (Stack Pointer) register is used to access items on the stack. The SP register points to the LAST value put on the stack.
The PUSH operation stores a value to the stack: PUSH AX ; SP= SP-2, M[SP]  AX
The “push AX” instruction is equivalent to: sub SP, 2 ; decrement SP by 2 for word operation mov [SP], AX ; write value to stack.
Stack access only supports 16-bit or 32-bit operations

## Slide 15: Visualizing the PUSH operation
lastvalue
????
????
????
????
????
????
????
????
high memory
low memory
 SP
before PUSH AX
lastvalue
ahal
????
????
????
????
????
????
????
high memory
low memory
 SP (new SP = old SP-2)
after PUSH AX
View memory as being 16 bits wide since stack operations are always 16 bit or 32 bits.
Notes: Use debug

## Slide 16: Multiple Pushes
lastvalue
????
????
????
????
????
????
????
????
high memory
low memory
 SP
before
lastvalue
ax
bx
cx
????
????
????
????
????
high memory
 SP
after all pushes
PUSH AX PUSH BX PUSH CX
low memory

## Slide 17: Reading Data from X86 stack via POP
The POP operation retrieves a value from the stack: POP AX ; AX  M[SP] , SP= SP+2
The “pop AX” instruction is equivalent to: mov AX, [SP] ; read value from top of stack add sp, 2 ; increment SP by 2 for word operation

## Slide 18: Visualizing the POP operation
FF65
23AB
????
????
????
????
????
????
????
high memory
low memory
 SP
before POP AX
FF65
23AB
????
????
????
????
????
????
????
high memory
low memory
 SP
AX = 23AB
after POP AX
View memory as being 16 bits wide since stack operations are always 16 bit or 32 bits.

## Slide 19: Visualizing multiple POP operations
FF65
23AB
357F
D21B
38AC
23F4
????
????
????
high memory
low memory
 SP
AX = 38AC BX = D21B CX = 357F
after all POPs
FF65
23AB
357F
D21B
38AC
23F4
????
????
????
high memory
low memory
 SP
before
pop AX pop BX pop CX

## Slide 20: Stack Overflow, Underflow
If you keep pushing data on the stack without taking data off the stack, then the stack can eventually grow larger than your allocated space
  Can begin writing to memory area that your code is in or other non-stack data
  This is called stack OVERFLOW
If you take off more data than you placed on the stack, then stack pointer can increment past the ‘start’ of the stack. This is stack UNDERFLOW.
Bottom line: You should allocate sufficient memory for your stack needs, and pop off the same amount of data as pushed in.

## Slide 21: Stack (summary)
Temporary storage
Segment and pointer SS:SP
Push and Pop (LIFO)
SP : top of the stack
After push SP is decremented

## Slide 22: Summary
Programs for 80x86
Machine language, Assembly, …
Registers, segments
Instruction set
Debug program
Stack