## Slide 1: Microprocessor System Design AVR Microcontroller Part 2
Omid Fatemi

## Slide 2: Jump & Call Chapter 3
The AVR microcontroller
and embedded
systems
using assembly and c

## Slide 3: Topics
Introduction to jump and call
Jump
Call
  Stack
  Calling a function
Time Delay

## Slide 4: Jump and Call
CPU executes instructions one after another.
  For example in the following C program, CPU first executes the instruction of line 3 (adds b and c), then executes the instruction of line 4.
1
2
3
4
5
6
void main ()
{
a = b + c;
c -= 2;
d = a + c;
}

## Slide 5: Jump and Call (Continued)
But sometimes we need the CPU to execute, an instruction other than the next instruction. For example:
  When we use a conditional instruction (if)
  When we make a loop
  When we call a function

## Slide 6: Jump and Call (Continued)
Example 1: Not executing the next instruction, because of condition.
  In the following example, the instruction of line 6 is not executed.
1
2
3
4
5
6
7
8
9
void main ()
{
int a = 2;
int c = 3;
if (a == 8)
c = 6;
else
c = 7;
c = a + 3;
}

## Slide 7: Jump and Call (Continued)
Example 2: In this example the next instruction will not be executed because of loop.
  In the following example, the order of execution is as follows:
    Line 4
    Line 5
    Again, line 4
    Again line 5
    Line 6
1
2
3
4
5
6
7
8
9
void main ()
{
int a, c = 0;
for(a = 2; a < 4; a++)
c += a;
a = c + 2;
}

## Slide 8: Jump and Call (Continued)
Example 3: Not executing the next instruction, because of calling a function.
  In the following example, the instruction of line 6 is not executed after line 5.
1
2
3
4
5
6
7
8
9
10
11
void func1 ();
void main ()
{
int a = 2, c = 3;
func1 ();
c = a + 3;
}
void func1 (){
int d = 5 / 2;
}
Code

## Slide 9: Jump and Call (Continued)
In the assembly language, there are 2 groups of instructions that make the CPU execute an instruction other than the next instruction. The instructions are:
  Jump: used for making loop and condition
  Call: used for making function calls

## Slide 10: Jump
Jump changes the Program Counter (PC) and causes the CPU to execute an instruction other than the next instruction.

## Slide 11: Jump
There are 2 kinds of Jump
  Unconditional Jump: When CPU executes an unconditional jump, it jumps unconditionally (without checking any condition) to the target location.
    Example: RJMP and JMP instructions
  Conditional Jump: When CPU executes a conditional jump, it checks a condition, if the condition is true then it jumps to the target location; otherwise, it executes the next instruction.

## Slide 12: Unconditional Jump in AVR
There are 3 unconditional jump instructions in AVR: RJMP, JMP, and IJMP
We label the location where we want to jump, using a unique name, followed by ‘:’
Then, in front of the jump instruction we mention the name of the label.
This causes the CPU to jump to the location we have labeled, instead of executing the next instruction.
1
2
3
4
5
LDI R16, 0
LDI R17, 2
L1: ADD R16, R17
RJMP L1
SUB R10,R15
Code
L1:
L1

## Slide 13: Ways of specifying the jump target
There are 3 ways to provide the jump address:
  PC = operand
  PC = PC + operand
  PC = Z register

## Slide 14: JMP
JMP PC = operand
  Example:
    Operand = 0000000000000000000110
1001 0100 0000 1100 0000 0000 0000 0110
1001 010X XXXX 110X XXXX XXXX XXXX XXXX XXXX XXXX

## Slide 15: JMP
0000
0000
0001
0002
0004
0005
0006
0006
0007
0009
.ORG 0
LDI R16, 15
LDI R17, 5
JMP LBL_NAME
LDI R18, 4
ADD R18, R17
LBL_NAME:
ADD R16,R17
JMP LBL_NAME
Code
Address
0006
opCode
operand
940C 0006
Machine code:
PC:
0000
0001
0002
0006
0007
In JMP, the operand, contains the address of the destination
When an JMP is executed:
  PC is loaded with the operand value
opCode
operand
940C 0006
Machine code:
0006

## Slide 16: RJMP (Relative jump)
RJMP PC = PC + operand
  Example:
    Operand = 000000000110
    PC = PC + 000000000110
1100 0000 0000 0110
1100 XXXX XXXX XXXX

## Slide 17: IJMP (Indirect jump)
IJMP PC = Z register
The instruction has no operand.
the Program counter is loaded with the contents of Z register.
  For example, if Z points to location 100, by executing IJMP, the CPU jumps to location 100.
1001 0100 0000 1001
Notes: X,Y,Z: Indirect Address Register
(X=R27:R26, Y=R29:R28 and Z=R31:R30)

## Slide 18: RJMP
0000
0000
0001
0002
0003
0004
0005
0005
0006
0007
.ORG 0
LDI R16, 15
LDI R17, 5
RJMP LBL_NAME
LDI R18, 4
ADD R18, R17
LBL_NAME:
ADD R16,R17
RJMP LBL_NAME
Code
Address
0005
opCode
operand
C002
Machine code:
PC:
0000
0001
0002
002
When RJMP is executed:
  The operand will be added to the current value of PC
opCode
operand
CFFE
Machine code:
FFE
+F
+0
0003
0005
0006
0007
0005

## Slide 19: Conditional Jump in AVR
The conditional jump instructions in AVR are as follows:
Instruction | Abbreviation of | Comment
BREQ lbl | Branch if Equal | Jump to location lbl if Z = 1,
BRNE lbl | Branch if Not Equal | Jump if Z = 0, to location lbl
BRCS lbl BRLO lbl | Branch if Carry Set Branch if Lower | Jump to location lbl, if C = 1
BRCC lbl BRSH lbl | Branch if Carry Cleared Branch if Same or Higher | Jump to location lbl, if C = 0
BRMI lbl | Branch if Minus | Jump to location lbl, if N = 1
BRPL lbl | Branch if Plus | Jump if N = 0
BRGE lbl | Branch if Greater or Equal | Jump if S = 0
BRLTlbl | Branch if Less Than | Jump if S = 1
BRHS lbl | Branch if Half Carry Set | If H = 1 then jump to lbl
BRHC lbl | Branch if Half Carry Cleared | if H = 0 then jump to lbl
BRTS | Branch if T flag Set | If T = 1 then jump to lbl
BRTC | Branch if T flag Cleared | If T = 0 then jump to lbl
BRIS | Branch if I flag set | If I = 1 then jump to lbl
BRIC | Branch if I flag cleared | If I = 0 then jump to lbl
SREG:
H
S
V
N
C
Z
T
I

## Slide 20: Usages of Conditional jump
Conditions
Loop

## Slide 21: Conditions
When b is subtracted from a:
  The result is zero, when a is equal to b
  Carry will be set when a < b
a
- b

## Slide 22: Example 1
Write a program that if R20 is equal to R21 then R22 increases.
Solution:
  SUB R20,R21 ;Z will be set if R20 == R21
  BRNE NEXT ;if Not Equal jump to next
  INC R22
  NEXT:

## Slide 23: Example 2
Write a program that if R26 < R24 then R22 increases.
Solution:
  SUB R26,R24 ;Z will be set if R20 == R21
  BRCC L1 ;if Carry cleared jump to L1
  INC R22
  L1:

## Slide 24: Example 3
Write a program that if R26 >= R24 then R22 increases.
Solution:
  SUB R26,R24 ;Z will be set if R20 == R21
  BRCS L1 ;if Carry set jump to L1
  INC R22
  L1:

## Slide 25: Example 4: IF and ELSE
R17 = 5;
if (R20 > R21)
R22++;
else
R22--;
R17 ++;
LDI R17,5
SUB R21,R20
BRCS IF_LABEL
DEC R22
JMP NEXT
IF_LABEL:
INC R22
NEXT:
INC R17

## Slide 26: Loop
Write a program that executes the instruction “ADD R30,R31” 9 times.
Solution:
.ORG 00
LDI R16,9 ;R16 = 9
L1: ADD R30,R31
DEC R16 ;R16 = R16 - 1
BRNE L1 ;if Z = 0
L2: RJMP L2 ;Wait here forever

## Slide 27: Loop
Write a program that calculates the result of 9+8+7+…+1
Solution:
.ORG 00
LDI R16, 9 ;R16 = 9
LDI R17, 0 ;R17 = 0
L1: ADD R17,R16 ;R17 = R17 + R16
DEC R16 ;R16 = R16 - 1
BRNE L1 ;if Z = 0
L2: RJMP L2 ;Wait here forever

## Slide 28: Loop
Write a program that calculates the result of 20+19+18+17+…+1
Solution:
.ORG 00
LDI R16, 20 ;R16 = 20
LDI R17, 0 ;R17 = 0
L1: ADD R17,R16 ;R17 = R17 + R16
DEC R16 ;R16 = R16 - 1
BRNE L1 ;if Z = 0
L2: RJMP L2 ;Wait here forever

## Slide 29: Loop
for (init; condition; calculation)
{
do something
}
END
calculation
Do something
Condition
No
Yes
init

## Slide 30: Loop
Write a program that calculates 1+3+5+…+27
Solution:
LDI R20,0
LDI R16,1
L1:ADD R20,R16
LDI R17,2
ADD R16,R17 ;R16 = R16 + 2
LDI R17,27 ;R17 = 27
SUB R17,R16
BRCC L1 ;if R16 <= 27 jump L1

## Slide 31: Call Topics
Stack, Push and Pop
Calling a function

## Slide 32: Stack
PUSH Rr
  [SP] = Rr
  SP = SP - 1
POP Rd
SP = SP + 1
Rd = [SP]
SP
Stack

## Slide 33: Stack
0000
0001
0002
0003
0004
0005
0006
0007
0008
0009
000A
000B
000C
000D
ORG 0
LDI R16,HIGH(RAMEND)
OUT SPH,R16
LDI R16,LOW(RAMEND)
OUT SPL,R16
LDI R20,0x10
LDI R21, 0x20
LDI R22,0x30
PUSH R20
PUSH R21
PUSH R22
POP R21
POP R0
POP R20
L1: RJMP L1
Address
Code
SP
Memory
R20:
R21:
$00
$10
$00
$20
$00
$00
$30
R22:
R0:
$10
$20
$30
0000

## Slide 34: Calling a Function
0000
0001
0002
0003
0004
0005
0006
0008
0009
000A
000A
000B
000C
000D
LDI R16,HIGH(RAMEND)
OUT SPH,R16
LDI R16,LOW(RAMEND)
OUT SPL,R16
LDI R20,15
LDI R21,5
CALL FUNC_NAME
INC R20
L1: RJMP L1
FUNC_NAME:
ADD R20,R21
SUBI R20,3
RET
Code
Address
0006
opCode
operand
940E 000A
Machine code:
SP
Stack
PC:
0004
0005
0006
000A
000B
000C
08
00
0008
0009
To execute a call:
  Address of the next instruction is saved
  PC is loaded with the appropriate value

## Slide 35: Time delay

## Slide 36: Time delay
LDI R16, 19
LDI R20, 95
LDI R21, 5
ADD R16, R20
ADD R16, R21
machine cycle
1
1
1
1
1
5

## Slide 37: Time delay
LDI R16, 100
AGAIN: ADD R17,R16
DEC R16
BRNE AGAIN
machine cycle
1
1
1
1/2
*100
*100
*100
Branch penalty
Notes: Cycles:
1 if condition is false
2 if condition is true

## Slide 38: Time delay
LDI R16, 50
AGAIN: NOP
NOP
DEC R16
BRNE AGAIN
machine cycle
1
1
1
1
1/2
*50
*50
*50
*50

## Slide 39: Time delay
LDI R17, 20
L1: LDI R16, 50
L2: NOP
NOP
DEC R16
BRNE L2
DEC R17
BRNE L1
machine cycle
1
1
1
1
1
1/2
1
1/2
*20
*20 * 50
*20 * 50
*20 * 50
*20 * 50
*20
*20

## Slide 40: I/O Ports in AVR
The AVR microcontroller
and embedded
systems
using assembly and c

## Slide 41: Topics
AVR pin out
The structure of I/O pins
I/O programming
Bit manipulating

## Slide 42: ATmega16/mega32 pinout
Vital Pins:
  Power
    VCC
    Ground
  Crystal
    XTAL1
    XTAL2
  Reset
I/O pins
  PORTA, PORTB, PORTC, and PORTD
Internal ADC pins
  AREF, AGND, AVCC
+5 V
+5 V
+5 V

## Slide 43: The structure of IO pins

## Slide 44: Example 1
Write a program that makes all the pins of PORTA one.
1 1 1 1 1 1 1 1
1 1 1 1 1 1 1 1
DDRA:
PORTA:
.INCLUDE “M32DEF.INC”
LDI R20,0xFF ;R20 = 11111111 (binary)
OUT PORTA,R20 ;PORTA = R20
OUT DDRA,R20 ;DDRA = R20

## Slide 45: Example 2
The following code will toggle all 8 bits of Port B forever with some time delay between “on” and “off” states:
LDI R16,0xFF ;R16 = 0xFF = 0b11111111
OUT DDRB,R16 ;make Port B an output port (1111 1111)
L1: LDI R16,0x55 ;R16 = 0x55 = 0b01010101
OUT PORTB,R16 ;put 0x55 on port B pins
CALL DELAY
LDI R16,0xAA ;R16 = 0xAA = 0b10101010
OUT PORTB,R16 ;put 0xAA on port B pins
CALL DELAY
RJMP L1

## Slide 46: Example 3
A 7-segment is connected to PORTA. Display 1 on the 7-segment.
ATmega32
8
PORTC
0
1
2
3
5
6
4
1 1 1 1 1 1 1 1
0 0 0 0 0 1 1 0
DDRC:
PORTC:
.INCLUDE “M32DEF.INC”
LDI R20,0x06 ;R20 = 00000110 (binary)
OUT PORTC,R20 ;PORTC = R20
LDI R20,0xFF ;R20 = 11111111 (binary)
OUT DDRC,R20 ;DDRC = R20
L1: RJMP L1

## Slide 47: Example 4
A 7-segment is connected to PORTA. Display 3 on the 7-segment.
ATmega32
8
PORTC
0
1
2
3
5
6
4
1 1 1 1 1 1 1 1
0 1 0 0 1 1 1 1
DDR:
PORTC:
.INCLUDE “M32DEF.INC”
LDI R20,0x4F ;R20 = 01001111 (binary)
OUT PORTC,R20 ;PORTC = R20
LDI R20,0xFF ;R20 = 11111111 (binary)
OUT DDRC,R20 ;DDRC = R20
L1: RJMP L1

## Slide 48: Example 5: Input
The following code gets the data present at the pins of port C and sends it to port B indefinitely, after adding the value 5 to it:
.INCLUDE "M32DEF.INC"
LDI R16,0x00 ;R16 = 00000000 (binary)
OUT DDRC,R16 ;make Port C an input port
LDI R16,0xFF ;R16 = 11111111 (binary)
OUT DDRB,R16 ;make Port B an output port(1 for Out)
L2: IN R16,PINC ;read data from Port C and put in R16
LDI R17,5
ADD R16,R17 ;add 5 to it
OUT PORTB,R16 ;send it to Port B
RJMP L2 ;continue forever

## Slide 49: Pull-up resistor

## Slide 50: The structure of I/O pins
PINx.n
DDRx.n
PORTx.n
INPUT
OUTPUT

## Slide 51: Out 0

## Slide 52: Out 1
1

## Slide 53: Example 6
Write a program that continuously sends out to Port C the alternating values of 0x55 and 0xAA.
  .INCLUDE "M32DEF.INC"
  LDI R16,0xFF ;R16 = 11111111 (binary)
  OUT DDRC,R16 ;make Port C an output port
  L1: LDI R16,0x55 ;R16 = 0x55
  OUT PORTC,R16 ;put 0x55 on Port C pins
  LDI R16,0xAA ;R16 = 0xAA
  OUT PORTC,R16 ;put 0xAA on Port C pins
  RJMP L1

## Slide 54: The structure of IO pins

## Slide 55: Input (Tri-state vs. pull up)

## Slide 56: Example 7
Write a program that reads from port A and writes it to port B.
.INCLUDE “M32DEF.INC”
LDI R20,0x0 ;R20 = 00000000 (binary)
OUT DDRA,R20 ;DDRA = R20
LDI R20,0xFF ;R20 = 11111111 (binary)
OUT DDRB,R20 ;DDRB = R20
L1: IN R20,PINA ;R20 = PINA
OUT PORTB,R20 ;PORTB = R20
RJMP L1

## Slide 57: I/O bit manipulation programming

## Slide 58: SBI and CBI instructions
SBI (Set Bit in IO register)
  SBI ioReg, bit ;ioReg.bit = 1
  Examples:
    SBI PORTD,0 ;PORTD.0 = 1
    SBI DDRC,5 ;DDRC.5 = 1
CBI (Clear Bit in IO register)
  CBI ioReg, bit ;ioReg.bit = 0
  Examples:
    CBI PORTD,0 ;PORTD.0 = 0
    CBI DDRC,4 ;DDRC.5 = 0

## Slide 59: Example
Write a program that toggles PORTA.4 continuously.
.INCLUDE “M32DEF.INC”
SBI DDRA,4
L1: SBI PORTA,4
CBI PORTA,4
RJMP L1

## Slide 60: Example
An LED is connected to each pin of Port D. Write a program to turn on each LED from pin D0 to pin D7. Call a delay module before turning on the next LED.
.INCLUDE "M32DEF.INC"
LDI R20, 0xFF
OUT DDRD, R20 ;make PORTD an output port
SBI PORTD,0 ;set bit PD0
CALL DELAY ;delay before next one
SBI PORTD,1 ;turn on PD1
CALL DELAY ;delay before next one
SBI PORTD,2 ;turn on PD2
CALL DELAY
SBI PORTD,3
CALL DELAY
SBI PORTD,4
CALL DELAY
SBI PORTD,5
CALL DELAY
SBI PORTD,6
CALL DELAY
SBI PORTD,7
CALL DELAY

## Slide 61: SBIC and SBIS
SBIC (Skip if Bit in IO register Cleared)
  SBIC ioReg, bit ; if (ioReg.bit = 0) skip next instruction
  Example:
    SBIC PIND,0 ;skip next instruction if PIND.0=0
    INC R20
    LDI R19,0x23
SBIS (Skip if Bit in IO register Set)
  SBIS ioReg, bit ; if (ioReg.bit = 1) skip next instruction
  Example:
    SBIS PIND,0 ;skip next instruction if PIND.0=1
    INC R20
    LDI R19,0x23

## Slide 62: Example
Write a program to perform the following:
(a) Keep monitoring the PB2 bit until it becomes HIGH;
(b) When PB2 becomes HIGH, write value $45 to Port C, and also send a HIGH-to-LOW pulse to PD3.
.INCLUDE "M32DEF.INC"
CBI DDRB, 2 ;make PB2 an input
SBI PORTB,2
LDI R16, 0xFF
OUT DDRC, R16 ;make Port C an output port
SBI DDRD, 3 ;make PD3 an output
AGAIN: SBIS PINB, 2 ;Skip if Bit PB2 is HIGH
RJMP AGAIN ;keep checking if LOW
LDI R16, 0x45
OUT PORTC, R16 ;write 0x45 to port C
SBI PORTD, 3 ;set bit PD3 (H-to-L)
CBI PORTD, 3 ;clear bit PD3
HERE: RJMP HERE

## Slide 63: Example
A switch is connected to pin PB0 and an LED to pin PB7. Write a program to get the status of SW and send it to the LED.
.INCLUDE "M32DEF.INC"
CBI DDRB,0 ;make PB0 an input
SBI DDRB,7 ;make PB7 an output
AGAIN: SBIC PINB,0 ;skip next if PB0 is clear
RJMP OVER ;(JMP is OK too)
CBI PORTB,7
RJMP AGAIN ;we can use JMP too
OVER: SBI PORTB,7
RJMP AGAIN ;we can use JMP too