## Slide 1: Microprocessor System Design
Omid Fatemi
(omid@fatemi.net)

## Slide 2: Class Work #11
AVR Timer - PWM

## Slide 3: Closed Book

## Slide 4: Questions
Explain the following items and express the size of each:
  OCR1A, OCR1B
  TCCR1A, TCCR1B
  TOV1, OCF1A
What is the function of waveform generator? Explain in general not in detail.

## Slide 5: Open-Note

## Slide 6: Problems
There are three buttons connected to PA.0, PA.1 and PA.2. PA.0 increases the speed of the motor, PA1 decreases and PA.2 stops the motor. Use the output of Timer 0 for making PWM signal. The clock frequency of AVR is 32MHz.
  Design the circuit. (use Darlington to drive the motor).
  Program Timer 0 (Phase correct PWM, clk / 8) and initialize the PWM output as 0.
  Draw the timing diagram of OC0, the value of TCNT0, TOV0, OCF. (OCR0=127)
  Write the program. (assume only one button is pressed at each time).
  With OCR0=32, calculate the average DC voltage to the motor and draw the timing diagram of OC0.