## Slide 1: Serial Communication
Omid Fatemi

## Slide 2: Outline
Serial vs. Parallel
RS-232
DTE, DCE
Flow control
Programming serial port
UART – 16550
UART in PC

## Slide 3: What is Serial Communications

## Slide 4: Serial Communication Types
Asynchronous
Synchronous
Transfer:
  Simplex
  Half duplex
  Full duplex

## Slide 5: Transfer Types

## Slide 6: Asynchronous Data Framing
Idle (high): Mark
Low: Space
Overhead? (parity, start, stop)

## Slide 7: Data Transfer Rate
Baud rate
bps

## Slide 8: RS-232 Standard
EIA 232 = ITU-T V.24/V.28
Specifies the interface between DTE and DCE:
  V.28 : mechanical and electrical characteristics
  V.24 : functional and procedural characteristics
Even used in applications where there is no DCE
  e.g. connecting computer to printer, magnetic card reader, robot, … etc.
Introduced in 1962 but is still widely used
Stand for Recommended Standard

## Slide 9: Vocabulary
DTE
  data terminal equipment
  e.g. computer, terminal
DCE
  data communication equipment
  connects DTE to communication lines
  e.g. modem

## Slide 10: DTE Connections

## Slide 11: RS-232

## Slide 12: Mechanical Characteristics
25-pin connector
  9-pin connector is more commonly found in IBM-PC but it covers signals for asynchronous serial communication only
Use male connector on DTE and female connector on DCE
Note: all signal names are viewed from DTE

## Slide 13: 25-Pin RS232 Connector
Source: Duck, Bishop & Read, Data Communications for Engineers, Addison-Wesley

## Slide 14: 9-Pin RS232 Connector

## Slide 15: Electrical Characteristics
Single-ended
  one wire per signal, voltage levels are with respect to system common (i.e. signal ground)
Mark: –3V to –15V
  represent Logic 1, Idle State (OFF)
Space: +3 to +15V
  represent Logic 0, Active State (ON)
Usually swing between –12V to +12V
Recommended maximum cable length is 15m, at 20kbps

## Slide 16: TTL to RS-232
Line drivers and line receivers

## Slide 17: RS-232 Frame Format
 |  |  | … |  |  |  | 
Start bit
ASCII
Parity
Stop bit
111101000001111
Idle
A
Example

## Slide 18: RS232 Logic Waveform

## Slide 19: Function of Signals
TD: transmitted data
RD: received data
DSR: data set ready
  indicate whether DCE is powered on
DTR: data terminal ready
  indicate whether DTR is powered on
  turning off DTR causes modem to hang up the line
RI: ring indicator
  ON when modem detects phone call

## Slide 20: Function of Signals
DCD: data carrier detect
  ON when two modems have negotiated successfully and the carrier signal is established on the phone line
RTS: request to send
  ON when DTE wants to send data
  Normally constantly ON in point-to-point lines
CTS: clear to send
  ON when DCE is ready to receive data
SG: signal ground
Notes:   RTS Used to turn on and off modem’s carrier signal in multi-point (i.e. multi-drop) lines

## Slide 21: Flow Control
Means to ask the transmitter to stop/resume sending in data
Required when:
  DTE to DCE speed > DCE to DCE speed
  (e.g. terminal speed = 115.2kbps and line speed = 33.6kbps, in order to benefit from modem’s data compression protocol)
    without flow control, the buffer within modem will overflow – sooner or later
  the receiving end takes time to process the data and thus cannot be always ready to receive

## Slide 22: Hardware Flow Control
RTS/CTS
  the transmitting end activates RTS to inform the receiving end that it has data to send
  if the receiving end is ready to receive, it activates CTS
  normally used between computer and modem
    computer is always ready to receive data but modem is not, because terminal speed > link speed

## Slide 23: Software Flow Control
Xon/Xoff
  when the buffer within the receiving end is nearly full, Xoff is sent to the transmitting end to ask it to stop
  when data have been processed by the receiving end and the buffer has space again, Xon is sent to the transmitting end to notify it to resume
  advantage: only three wires are required (TD, RD and GND)
  disadvantage: confusion arises when the transmitted data (e.g. a graphics file) contains a byte equal to 13H (Xoff)

## Slide 24: RS-232 (con)
Communication between two nodes
x-off
x-on
data transmission
transmitter
receiver
receiver
RTS
RTS
RTS
CTS
CTS
TD
CTS
RD
transmitter
data transmission
Are you ready to receive?
No
Yes
Send character
Software Handshaking
Hardware Handshaking
Notes: Software flow control uses special characters to control the flow of data when a device wishes to halt the flow it sends the XOFF character, when flow can resume it sends the XON character. The XOFF character is called DC3 or Device Code 3. It is decimal 19 or control S. The XON character is called DC1 or Device Code 1. It is decimal 17 or control Q.
XOn / XOff is a software flow control mechanism. It can only be used in character oriented data transmissions (not binary transfer) as it relies on the use of a pre-determined XOn character and a pre-determined XOff character. The basic idea is simple, when the receiver buffer fills to the point it cannot receive anymore data it issues an XOff (Transmit Off) to the transmitter. When the transmitter sees the XOff character is stops transmitting. It will only resume once it sees a corresponding XOn. The disadvantage of such a system is that should an issued character become damaged in transit no action will be taken by the transmitter.

## Slide 25: Null Modem Cables
Used to directly connect two DTEs together
Many possibilities – depending on whether and how the two DTEs handshake (i.e. doing flow control)

## Slide 26: Null Modem Cables Examples
Source: Horowitz and Hill, The Art of Electronics, Cambridge University Press

## Slide 27: Other Standards