## Slide 1: Microprocessor System Design
Omid Fatemi
8088 Microprocessor
(omid@fatemi.net)

## Slide 2: Outline
Pin configuration
Minimal / Maximal mode
Address latch enable
Bi-directional data bus

## Slide 3: The Microprocessor
An integrated circuit with millions of transistors interconnected with very small aluminum wires.
Controls and directs activities of the computer.
Execute stored programs.

## Slide 4: Von Neumann Architecture
Memory
Data
Microprocessor
Registers
Actual
Processor
Program
Address Lines
Data Lines
Control Lines

## Slide 5: The 8086 Family:the Late 1970’s
Could address up to 1 mb of memory at a time when other CPU’s could only address 64 kb.
The 16 bit external bus too powerful.
The 8088 replaced the 8086 and had only an 8 bit external bus.
The 8088 CPU was the first chip used in IBM’s microcomputers.
8088
  Data is organized into byte widths
  The 1MB memory is organized as 1M x 8-bits
8086/80186
  Data is organized into word widths
  The 1MB memory is organized as 512k x 16-bits

## Slide 6: The 80286 Family:1983
Wanted to make the 286 backward compatible with the 8088’s.
So had 2 modes:
  Real mode-less powerful.
  Protected mode-very powerful.
    Could access up to 16 mb of memory.
    Needed a special operating system.
    But most users only had DOS.
80286/80386SX
  Data is organized into word widths
  The 16MB memory is organized as 8M x 16-bits

## Slide 7: The 386 DX: 1985
First true 32 bit chip, all buses 32 bits wide
Capable of running in real mode, 286 protected mode and its own 386 protected mode
In 386 protected mode it had 2 new functions:
  Virtual memory- could use hard drive to pretend that computer had up to 4 GB of data!
  Virtual 8086- 8086 bubbles created for DOS
• 80386DX/80486
  Data is organized into double word widths
  The 4GB memory is organized as 1G x 32-bits

## Slide 8: The 386 SX:1988
How different from the 386DX?
  External data bus reduced to 16 bits
  Address bus reduced to 24 bits, which limited memory use to 16 mb
  First popular laptops were based on the 386SX but was called the 386 SL and ran on 3.3 volts

## Slide 9: The 486DX:1989
How different from the 386 family?
  A built in math coprocessor.
    Performs high math functions.
  A built in 8K cache on same chip.
    This was an SRAM cache that stores code read in the past. When the CPU asks for the code again, it doesn’t have to go to DRAM to get it.

## Slide 10: 486SX:1991
Same as 486 DX except the math co-processor is disabled.

## Slide 11: The Pentiums:1993
Had 64 bit external data bus that split internally as 2 dual pipelined 32 bit buses
Supported an 8K write through cache for programs
Most early Pentiums ran at 3.3 volts. This conserved heat. Voltage regulators on the motherboard can decrease voltage
Includes clock doubling through the setting of jumpers

## Slide 12: Recent Pentiums:after 1996
MMX- helps with multimedia products
Increased multipliers/clocks
Improved processing- better cache branch predicting
Improved superscalar architecture
SSE/SSE2 instructions
• Pentium Pro/Pentium 1-4
  Data is organized into quad word widths
  The 4GB memory is organized as 512MB x64-bits
(on P2-4, actual address bus is 36 bits)

## Slide 13: 8088 Microprocessor
Minimum Mode

## Slide 14: Pin Configuration

## Slide 15: Power and Ground Pins
Vcc – pin 40
Gnd – pin 1 and 20

## Slide 16: Address Pins
AD0..AD7
A8..A15
A19/S6, A18/S5, A17/S4, A16/S3

## Slide 17: Data Pins
AD0..AD7

## Slide 18: Control Pins
MN/MX’ (input)
  Indicates what mode the processor is to operate in
READY (input)
  When given an input LOW, it will go into a wait state
CLK (input)
  Provides basic timing for the processor
RESET (input)
  Causes the processor to immediately terminate its present activity
  To reset the microprocessor, this must be HIGH for at least 4 clock cycles

## Slide 19: Control Pins
TEST’ (input)
  Connect this to HIGH
HOLD (input)
  Connect this to LOW
HLDA (output)

## Slide 20: Control Pins
INTR (input)
  Interrupt request
INTA’ (output)
  Interrupt Acknowledge
NMI (input)
  Non-maskable interrupt

## Slide 21: Control Pins
DEN’ (output)
  Data Enable
  It is LOW when processor wants to receive data or processor is giving out data
DT/R’ (output)
  Data Transmit/Receive
  When HIGH, direction of data lines is from microprocessor to memory/devices
  When LOW, direction of data lines is from memory/devices to microprocessor
IO/M’ (output)
  Device/Memory
  When HIGH, microprocessor wants to access I/O Device
  When LOW, microprocessor wants to access memory

## Slide 22: Control Pins
RD’ (output)
  When LOW, it indicates that the microprocessor is performing a read access
WR (output)
  When LOW, it indicates that the microprocessor is performing a write access
ALE (output)
  Address Latch Enable
  Provided by the microprocessor to latch address
  When this is HIGH, microprocessor is using AD0..AD7, A19/S6, A18/S5, A17/S4, A16/S3 as address lines

## Slide 23: Clock Signal
needed by the microprocessor to synchronize signals
ideally a square wave having a constant frequency

## Slide 24: 8086 Signals

## Slide 25: Providing Clock, Reset, and Ready Signal
8284A

## Slide 26: Minimum Mode