## Slide 1: Microprocessor System Design Input / Output Peripheral Interfacing
Omid Fatemi
(omid@fatemi.net)

## Slide 2: Outline
Peripheral devices
  Input devices
  Output devices
8 bit / 16-bit IO
Simple Output device - interfacing LEDs
Simple Input device - interfacing switches

## Slide 3: Peripheral
is an input and/or output device
like a memory chip, it is mapped to a certain location (called the port address)
unlike a memory chip, a peripheral is usually mapped to a single location

## Slide 4: Output Device
like a memory chip, you can write to an output device
You can write to a memory chip using the command mov [bx], al
You can write to an output device using the command out dx, al

## Slide 5: Input Device
like a memory chip, you can read from an input device
You can read from a memory chip using the command mov al, [bx]
You can read from an input device using the command in al, dx

## Slide 6: Memory mapped vs. peripheral
Same instruction vs. independent instruction
Entire address bus vs. part of address bus
Same control signals vs. independent
More IO ports vs. 65536 ports
More commands and operations
Uses memory space

## Slide 7: Two formats for IN / OUT
Format 1
IN AL, port#
Or
OUT port#, AL
Example:
  BACK: IN AL,22H CMP AL, 100 JNZ BACK
Format 2
MOV DX,port# IN AL, DX
Or
MOV DX, port# OUT DX, AL

## Slide 8: 8bit vs 16bit IO
8088 case:
MOV DX, 648H OUT DX, AX ;AX = 76A9H
Address bus and ALE
Low byte (A9), IOW
Setup time
Address (649) and ALE
High byte (76), IOW
Setup time
8086 case:
MOV DX, 648H OUT DX, AX ;AX = 76A9H
Address bus and ALE
Word (76A9), IOW
Setup time

## Slide 9: Creating a Simple Output Device
Use 8-LED’s

## Slide 10: Use 8 LED’s
8088
Minimum
Mode
A18
A0
:
D7
D6
IOR
IOW
A19
D5
D4
D3
D2
D1
D0
:
mov al, 55
out dx, al
:
:
:

## Slide 11: Creating a Simple Output Device
Use 8-LED’s
Use a chip and an address decoder such that the LED’s will respond only to the command out and a specific address (let’s assume that the address is F000)

## Slide 12: Use of 74LS245 and Address Decoder
:
mov al, 55
mov dx, F000
out dx, al
:
8088
Minimum
Mode
A18
A0
:
D7
D6
IOR
IOW
A19
D5
D4
D3
D2
D1
D0
74LS245
B0
B1
B2
B3
B4
B5
B6
B7
A0
A1
A2
A3
A4
A5
A6
A7
E
DIR
5V
A
1
5
A
1
4
A
1
3
A
1
2
A
1
1
A
1
0
A
9
A
8
A
7
A
6
A
5
A
4
A
3
A
2
A
1
A
0
IOW

## Slide 13: Creating a Simple Output Device
Use 8-LED’s
Loses the data
Solution?
Use a chip and an address decoder such that the LED’s will not only respond to the command out and a specific address (let’s assume that the address is F000) but will also latch the data

## Slide 14: Use of 74LS373 and Address Decoder
:
mov al, 55
mov dx, F000
out dx, al
:
A
1
5
8088
Minimum
Mode
A18
A0
:
D7
D6
IOR
IOW
A19
D5
D4
D3
D2
D1
D0
A
1
4
A
1
3
A
1
2
A
1
1
A
1
0
A
9
A
8
A
7
A
6
A
5
A
4
A
3
A
2
A
1
A
0
IOW
74LS373
Q0
Q1
Q2
Q3
Q4
Q5
Q6
Q7
D0
D1
D2
D3
D4
D5
D6
D7
OE
LE

## Slide 15: Creating a Simple Input Device
Use 8-Switches (keys)
Use a chip and an address decoder such that the keys will be read only to the command in and a specific address (let’s assume that the address is F000)
How to interface a switch to computer?

## Slide 16: Use of 74LS245 and Address Decoder
:
mov dx, F000
in al, dx
:
A
1
5
8088
Minimum
Mode
A18
A0
:
D7
D6
IOR
IOW
A19
D5
D4
D3
D2
D1
D0
A
1
4
A
1
3
A
1
2
A
1
1
A
1
0
A
9
A
8
A
7
A
6
A
5
A
4
A
3
A
2
A
1
A
0
IOR
5V
74LS245
B0
B1
B2
B3
B4
B5
B6
B7
A0
A1
A2
A3
A4
A5
A6
A7
E
DIR
Same address for input and output?

## Slide 17: How do you know if a user has pressed a button?
By Polling
By Interrupt

## Slide 18: Polling
mov dx, F000
L1: in al, dx
cmp al, FF
je L1
:
:
A
1
5
8088
Minimum
Mode
A18
A0
:
D7
D6
IOR
IOW
A19
D5
D4
D3
D2
D1
D0
74LS245
B0
B1
B2
B3
B4
B5
B6
B7
A0
A1
A2
A3
A4
A5
A6
A7
E
DIR
A
1
4
A
1
3
A
1
2
A
1
1
A
1
0
A
9
A
8
A
7
A
6
A
5
A
4
A
3
A
2
A
1
A
0
IOR
5V

## Slide 19: Output Port Design
T1 – T4 of OUT 99H, AL ?

## Slide 20: Input Port Design
T1 – T4 of IN AL, 5FH ?