## Slide 1: Microprocessor System Design IO Applications
Omid Fatemi
(omid@fatemi.net)

## Slide 2: ADC and DAC Programming in AVR
The AVR microcontroller
and embedded
systems
using assembly and c

## Slide 3: Topics

## Slide 4: Outline
DAC (Digital to Analog Converter)
ADC (Analog to Digital Converter)
ADC major characteristics
ADC in AVR
AVR ADC Programming
  ADCH and ADCL
  ADMUX
  ADCSRA
Signal conditioning and sensors
PWM (pulse width modulation) signals
DC motor control

## Slide 5: DAC
What is DAC ?
How to connect an DAC to micro?

## Slide 6: 8-bit R-2R Ladder Digital To Analog Converter

## Slide 7: Digital to Analog Converter

## Slide 8: Example – Step Ramp

## Slide 9: What is ADC? Do we need it?
Analogue vs. digital signal

## Slide 10: ADC major characteristics
Conversion Time
Resolution
Vref
Parallel vs. serial
Input channels
Step Size

## Slide 11: Some of ADC Signals
Dout = Vin / Step size
  ( in 8 bit ADC and Vref = 2.56 what is D out for 20mV input voltage?)
Start of Conversion
Channel Selector

## Slide 12: Analog to Digital
F = / (1.1 RC), 66 cycles
R = 10k, C= 150 pico, f =606khz , conversion 110 micro sec
Notes: F = / (1.1 RC), 66 cycles
R = 10k, C= 150 pico, f =606khz , conversion 110 micro sec

## Slide 13: Vin Range

## Slide 14: Timing
When intr is cleared?

## Slide 15: Interfacing ADC

## Slide 16: Example

## Slide 17: ADC in AVR (Atmega 16/32)
10-bit Resolution
65 - 260 μs Conversion Time
Up to 15 kSPS at Maximum Resolution
8 analogue input channel
7 differential input channel
2 differential input channel with 10x or 200x gain
3 source of Vref
Internal 2.56V Vref generator
Free Running or Single Conversion Mode
Interrupt on ADC Conversion Complete
Notes:   • 0.5 LSB Integral Non-linearity
  • ±2 LSB Absolute Accuracy
8 Multiplexed Single Ended Input Channels
• 7 Differential Input Channels
• 2 Differential Input Channels with Optional Gain of 10x and 200x(1)
• Optional Left adjustment for ADC Result Readout
• 0 - VCC ADC Input Voltage Range
• Selectable 2.56V ADC Reference Voltage
• ADC Start Conversion by Auto Triggering on Interrupt Sources

## Slide 18: Hardware Consideration

## Slide 19: ADCH and ADCL Data registers
ADCH:ADCL store the results of conversion.
The 10 bit result can be right or left justified:
ADLAR = 0
ADLAR =1

## Slide 20: ADMUX

## Slide 21: ADC input selection

## Slide 22: ADCSA

## Slide 23: ADC Prescaler
PreScaler Bits let us change the clock frequency of ADC
The frequency of ADC should not be more than 200 KHz
Conversion time is longer in the first conversion

## Slide 25: Programming ADC

## Slide 26: Signal conditioning
Thermo couple provides temp in form of uV
PT100 provides temp in form of resistance
Some humidity sensor provide the result in form of Capacitance
-> We have to change these signals to Voltage to convert it by ADC
    This job is called signal conditioning

## Slide 27: Sensor Interfacing

## Slide 28: Temperature Sensor

## Slide 29: Pulse width modulator
clk
pwm_o
25% duty cycle – average pwm_o is 1.25V
clk
pwm_o
50% duty cycle – average pwm_o is 2.5V.
clk
pwm_o
75% duty cycle – average pwm_o is 3.75V.
Generates pulses with specific high/low times
Duty cycle: % time high
  Square wave: 50% duty cycle
Common use: generate clock like signals for another device, or control average voltage to an electric device
  Simpler than DC-DC converter or digital-analog converter
  DC motor speed, dimmer lights
Another use: encode commands, receiver uses timer to decode
  1 ms interval  command A
  2 ms interval  command B
  4 ms interval  command C, etc.
- 5V
- 0V
- 5V
- 0V
- 5V
- 0V
- 5V
- 0V
- 5V
- 0V
- 5V
- 0V

## Slide 30: Controlling a DC motor with a PWM
void main(void){
/* controls period */
PWMP = 0xff;
/* controls duty cycle */
PWM1 = 0x7f;
while(1){};
}
The PWM alone cannot drive the DC motor, a possible way to implement a driver is shown below using an NPN transistor.
Internal Structure of PWM
clk_div
cycle_high
(8 bit)
8bit counter
( 0 – 254)
8-bit
comparator
controls period  how fast the counter increments
counter ≤ cycle_high,
pwm_o = 1
counter≥cycle_high,
pwm_o = 0
pwm_o
clk
Relationship between applied voltage and speed of the DC Motor
DC
MOTOR
5V
From processor
We wish to control the speed of a DC motor, which is proportional to the voltage applied to the motor. PWM can be used to provide average voltages to control the motor rpm.
Cycle_high = FF  duty=100% Cycle_high = 7F  duty = 50%
Cycle_high = 00  duty = 0%
5V
B
A

## Slide 31: Printer Connection

## Slide 32: IO Base Address for LPT

## Slide 33: Printer’s Ports

## Slide 34: Selected Problems (Ch. 4)